## Slide 1
AirSense
Predicting the evening air-quality peak before it arrives.
25.8% better than the naive baseline · R² 0.801
peak
forecast
measured
Amaan Khan · Srishti Rathi
Maharaja Agrasen Institute of Technology, Delhi · 1M1B Portfolio Submission
Notes: AirSense forecasts the hyper-local NOx peak 1-6 hours ahead and attaches a recommended action. Built by Amaan Khan and Srishti Rathi at MAIT Delhi. Everything you will see is computed from real sensor data and validated on a held-out test set.

## Slide 2
The air goes bad before anyone knows
Delhi NCR — and specifically our own campus, which we audited on foot.
Government monitoring stations report city-wide conditions, and they report them after the fact. On a campus that means the decision people actually face — should this session move indoors, should the gate queue be staggered — is always made too late.
1
Students
Outdoor sessions, sport and assembly sit in the evening peak.
2
Staff
No advance signal to reschedule activity or raise filtration.
3
Commuters
The gate and parking areas are the most traffic-exposed points on site.
MEASURED IN OUR OWN DATA
3.3×
higher NOx in the 6–9 PM window than overnight
175.1 ppb evening mean (18:00–21:00)
53.3 ppb overnight mean (03:00–06:00)
Computed live from 2,000 hourly readings — never hardcoded.
Pollution here is not random noise. It is a daily cycle that tracks traffic — which is exactly what makes it forecastable.
Notes: We did not start from a hypothetical. We audited our own campus on foot, defined indicators, then went looking for data. The number that matters: evening NOx runs 3.3 times overnight levels. Pollution is a predictable daily cycle, not random.

## Slide 3
What the data actually says
UCI Air Quality Data Set (De Vito et al., 2008) — 2,000 contiguous hourly readings.
Chart: Hour of day
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Mean NOx (ppb) | 95.9 | 69.6 | 48.3 | 48.5 | 35.3 | 46 | 83.5 | 175.4 | 219.7 | 210.8 | 179.3 | 153.6 | 135.2 | 128.5 | 122.5 | 125.4 | 128.8 | 152.4 | 175.9 | 198.4 | 187.8 | 138.3 | 111.6 | 111.1
Bars use the same risk bands as the app: green below 100 ppb, amber 100–200, orange above 200. Two peaks are visible — the morning rush and the 6–9 PM window (hours 18–21).
HOW WE PREPARED IT
Replaced the −200 sensor-failure sentinel with null
Dropped rows with no target value
Forward-fill, then median-fill, remaining gaps
Removed duplicate timestamps
Sorted chronologically
This mirror was already cleaned upstream, so the sentinel pass replaced 0 values. We report that rather than claim credit for it.
11 Mar – 23 Jun 2004 · hourly · 63 non-hourly gaps noted
Evening peak averages 3.3× overnight levels — 175.1 ppb versus 53.3 ppb.
Notes: We used the UCI hourly air-quality dataset. Cleaning is real code and it is honest: this particular mirror was pre-cleaned, so the sentinel pass found zero values to replace, and we say so. The daily cycle is unmistakable - a morning rush peak and an evening peak, with an overnight trough.

## Slide 4
How AirSense works
Time-series regression: continuous, timestamped data with a strong daily cycle.
Data
Cleaning
Features
Model
Forecast
Action
1
Gradient boosting, not an LSTM
About 2,000 rows of tabular lagged features. It trains in seconds and its feature importances are directly inspectable — a deliberate trade-off, not a shortcut.
2
Every feature is lagged
CO and NOx correlate at 0.94 here. Using same-hour co-pollutants would be nowcasting dressed as forecasting, so weather and co-pollutants are lagged by one hour.
3
One shared feature module
app/features.py is imported by both training and serving, so the two cannot silently drift apart — the classic way a forecasting project breaks.
BUILT WITH
Python · scikit-learn · pandas
FastAPI · Uvicorn
Chart.js · Tailwind CSS
Docker · Google Cloud Run
Claude Code (AI assistance)
One Cloud Run service serves the API and the UI.
Prediction target: NOx concentration, 1 to 6 hours ahead, with a recommended action attached to every hour.
Notes: The pipeline is data, cleaning, features, model, forecast, action. We chose gradient boosting because the dataset is small and tabular and we wanted inspectable feature importances. The critical detail is that every feature is lagged - the model only ever sees the past.

## Slide 5
The live prototype
Deployed and public — no login required.
airsense-526660427489.asia-south1.run.app
!
Peak predicted in 2 hours — act now.
Forecast reaches 239.7 ppb (High) at 08:00. Move outdoor sessions indoors.
WHAT A USER DOES
Opens the link, reads the current band and the action for right now, then checks the six forecast cards for the next window worth acting on.
Dashboard
Current reading, risk band, recommended action, and the six-hour forecast strip.
Forecast
Measured 48 hours joined to the prediction, hour-by-hour table, CSV export.
Model Performance
Backtest of predicted against actual, plus early-warning skill.
Because the dataset is historical, "now" is a position you choose — a judge can move the replay point and watch the model re-forecast from only the data before that hour.
Notes: This is live and public. Open the link, and the dashboard shows the current reading with a risk band and the action to take. The orange banner is the whole product thesis: the peak is two hours away and here is what to do about it. Six screens behind a sidebar.

## Slide 6
Validated, not asserted
Held-out chronological test set — 396 hours the model never saw in training.
Chart: MAE (ppb) — lower is better
| AirSense | Persistence baseline
Mean absolute error (ppb) | 25.92 | 34.94
25.8%
lower error than baseline
0.801
R² on held-out test set
1,580 / 396
train / test rows
86.4%
hours within 50 ppb
EARLY WARNING · ONE HOUR AHEAD
Of 72 hours that actually exceeded 200 ppb, the model flagged 52 — 72.2% caught, 77.6% of warnings correct. 20 missed, 15 false alarms.
Chronological split — no future data leaked into training. Baseline is "persistence": next hour equals current hour, the honest naive benchmark.
Known limits: one sensor stream, so the four campus zones are simulated and labelled as such · historical data, not a live feed · exogenous features held constant · risk bands are project-defined, not CPCB standards.
Notes: This is the slide most teams will not have. Our MAE is 25.92 against a persistence baseline of 34.94 - 25.8 percent better, R squared 0.801, on a chronological split so no future data leaked. And the operational number: of 72 hours that actually went High, we flagged 52 an hour ahead. We report the 20 misses and 15 false alarms too.

## Slide 7
Impact potential
What changes when a campus can see the peak an hour or more before it lands.
1
Environmental
Targeted filtration and ventilation instead of running it blind all day.
Advance notice supports staggering exit timings to flatten the gate-queue peak.
Measured capability: 72.2% of High-pollution hours flagged one hour ahead.
2
Social
Sensitive and asthmatic individuals get a decision, not just a number.
Outdoor sport and assembly can be scheduled into cleaner windows.
The zone design lets guidance be location-specific rather than campus-wide.
3
Governance
Every figure in the interface is computed from real data; anything derived is labelled simulated.
Validation, limitations and data provenance are published in the repository.
Forecasts export to CSV with provenance headers for audit.
Who benefits first: roughly the whole campus population passing the Main Gate and Parking Block, the two most traffic-exposed points in our design. Quantified ESG targets are carried over from Assignment 4A.
Notes: Impact splits three ways. Environmental: filtration and scheduling become targeted instead of blind. Social: sensitive individuals get an actionable decision. Governance: every number is traceable and anything simulated is labelled. Add your Assignment 4A quantified ESG targets to the bar at the bottom.

## Slide 8
What's next
The single biggest accuracy win available to us is a weather forecast — it is the one assumption we currently hold constant.
1
Pilot
Deploy a real low-cost NOx sensor at MAIT and replace the historical file with a live feed.
2
Multi-zone
Additional sensors turn the four simulated zones into four measured ones.
3
Forecast quality
Ingest a weather forecast so exogenous features stop being held constant.
4
Alerting
Opt-in notifications ahead of predicted Severe hours.
5
Scale
Multi-campus tenancy and a documented public API.
SUPPORT NEEDED
A calibrated reference-grade sensor for validation
Permission for on-campus sensor placement
Cloud credits beyond the trial tier
Live app · airsense-526660427489.asia-south1.run.app
Code · github.com/Rex123-hash/Air-Sense
Notes: Next step is a real sensor pilot on campus. The honest gap in the model today is that we hold weather constant - a forecast feed is the biggest single improvement available. We need a reference sensor for validation, placement permission, and credits beyond the trial tier.